## Slide 1: Chip Experiment Setup

## Slide 2: Comparison with SOA 1

## Slide 3: Comparison with SOA
 | Caviglia et al. (2016) | Khalil et al. (2018) | Simmich et al. (2023) | Lee et al. (2024) | Alea et al. (2024) | Narayanan et al. (2023)
Sensor | POSFET | POSFET | PiezoFET | Triboelectric Nanogenerator (TENG) | PVDF-based Piezo | General purpose
Encoding Scheme | SA (using + and - LIF) | Extension of Caviglia et al. | SA | SA | FA with exponential decay | FA + SA
Input Frequency | 1-1000 Hz | Sensitivity to input signal increased | < 1 kHz | Tested with a shaker at 1 Hz | 0.1-1 kHz | 0.1-100kHz
Output Frequency | 1.2-50 kHz | Lower Output Frequency | < 180 Hz | 10 Hz -3 kHz | ? | 0.1-100kHz
Sensitivity (Hz/N) | 40k |  | 200 | (2-60 N) | 0.4fF p-p input referred charge noise | 1.4uV input referred noise

## Slide 4: Desired Chip Performance 2

## Slide 5: Stimulus Characterization 2.1

## Slide 6: Stimulus Characterization
In the SOA, most papers have done only electric characterization of the proposed device.
Two types of stimulus : static and dynamic.
For both types, both electrical and mechanical (sensor) characterization should be done (on 1 taxel and on groups of taxels to study the mismatch).
For mechanical characterization, a useful test would be to plot the instantaneous output frequency of the SA for different stimuli strength.

## Slide 7: Drift Characterization
In Caviglia et al. (2016), a drift characterization has been performed.
                => Drift with a pseudo-exponential slope of 1.2V with a time constant of 640 seconds.
For our test, acquisition of the Vin and Vdiff for t seconds for a constant stimulus (after reset pulse for capacitive amplifier).

## Slide 8: Fast Adapting Circuit 2.2

## Slide 9: Fast Adapting Circuit
FA-I : 3-40 Hz
FA-II : 40-500 Hz
Few Hz to 1kHz
Biology Aspect
Engineering Aspect

## Slide 10: Slow Adapting Circuit 2.3

## Slide 11: Slow Adapting Circuit
SA-I : 0.3-4 Hz
SA-II : 100-500 Hz
Few Hz to 500Hz
Biology Aspect
Engineering Aspect
Might be difficult to properly characterize the SA behavior due to the drift in the input voltage.

## Slide 12: ATIS Circuit 2.4

## Slide 13: ATIS Circuit
The ATIS performance should be able to match the FA max output firing rate.
The second threshold crossing generated spike should happen before a new spike from the FA is triggered.

## Slide 14: FA and SA Circuits
Operation corners should be tested for the FA and SA circuits :
Very low strength stimulus (few mV p2p) with high/low amplification gain
Very high strength stimulus (around 1V p2p) with low/high amplification gain
Diverse stimuli shapes (square and sinusoidal) and frequencies (10 Hz to 1 kHz) should
also be tested (first electrically and then mechanically).

## Slide 15: Miscellaneous Tests and Metrics 2.5

## Slide 16: Event communication
The AER performance should be tested (in the worst case) with high firing activity from the FA and the SA simultaneously for many taxels at the same time.
                => Quantify maximal frequency of operation of the AER.
In case of maximal frequency of operation of the AER, the communication scheme used between the chip and the FPGA should not introduce any latency.
  => Rate of transmission should be > fmax of AER.
Test the Snowball AER to quantify the delay for a spike generated at the beginning of the array to arrive at the output of the SNBL.

## Slide 17: Data Stream
In order to set the biases and parameters of the chip, the digital stream of data should be quick enough not to see any latency.
=> should take a few milliseconds (or less). As long as it is not in the order of seconds.
There are two different data streams going through the chip (one for the main circuits and one for the test circuits).
Testing the correct functioning of the data stream could then be done first with the test circuits as it is relatively short.

## Slide 18: Reset and Triggers
Test to check whether the chip behaves correctly when the reset is activated.
Test whether a specific circuit in a certain taxel can correctly be disabled and does not generate spikes when it should not.
Test the global trigger of the ATIS circuit.

## Slide 19: Power consumption
In many papers of the SOA, the power consumption is given per taxel or for the entire chip with no specification on the activity of the chip.
One better approach would be to compute it for different output frequencies (either only FA + ACE or FA + SA or per single modality). :
                - Per taxel.
                - For the entire taxel array.
                - For the entire chip (without test circuits or Groenigen circuits).
Need to plan for power measurements on the FPGA/computer.

## Slide 20: Connections to the chip
We have 256 pads on the chip.
There are 66 taxels that necessitate an input. It should either be connected to a DAC (to generate synthetic input signals) or to a sensor (to treat mechanical stimuli).
The digital pins of the chip (input/output) should be handled by the FPGA (?).
The analog pins (excluding the taxels pads) should either be connected to ADC or DAC.
Can the FPGA handle everything ? (Data stream, AER communication, reading of debug signals).

## Slide 21: Similar setup for the test circuits
For the test circuits, the events are directly assigned to a distinct pad of the chip.
=> Connected to FPGA for processing.
For the analog inputs, it should either be connected to a DAC (to generate synthetic input signals) or to a sensor (to treat mechanical stimuli).

## Slide 22: Software Development and FPGA
Can the software be developed independently from the FPGA ?
Do we need anything else than ADCs, DACs and the FPGA ? How to connect the sensors to the chip (connection from the sensor to the PCB then to the chip) ? What about additional noise ?